IEEE Conference on Factory Communication
Simulating Time-Sensitive Networking using OMNeT++/INET Framework
WFCS – June 10-13, 2025
Levente Mészáros, OpenSim Ltd.

---
Introduction to OMNeT++
- Simulator for communication networks
- Modular and C++-based
- Open source model libraries
- Widely used in research
- Free for academic use
- Commercial version: OMNEST
omnetpp.org
omnest.com

---
Introduction to INET Framework
- Model library for wired and wireless networks
  - Internet protocols, routing protocols, etc.
  - Applications, queueing models, clock, etc.
  - Mobility, power consumption, physical environment, etc.
- Open source
- Well-documented
- Built for experimentation
inet.omnetpp.org

---
Relevance to Factory Automation
- Support for Time-Sensitive Networking (IEEE)
  - 802.3br Frame Preemption
  - 802.1Qbv Time-Aware Traffic Shaping
  - 802.1Qav Credit-Based Shaper
  - 802.1Qcr Asynchronous Traffic Shaping
  - 802.1Qci Per-Stream Filtering and Policing
  - 802.1AS Time Synchronization
  - 802.1CB Frame Replication and Elimination
  - 802.1cg 10BASE-T1S
- Extensible with Profinet, EtherCAT, etc.
- Allows analyzing custom and diverse industrial networks

---
Covered Topics
Cut-through switching
Frame preemption
Per-stream filtering and policing
Scheduling and traffic shaping
Automatic gate schedule configuration
Time synchronization
Frame replication and elimination for reliability

---
Covered Topics
Cut-through switching
Frame preemption
Per-stream filtering and policing
Scheduling and traffic shaping
Automatic gate schedule configuration
Time synchronization
Frame replication and elimination for reliability

---
Store-and-forward Switching
Receive whole frame before forwarding
Incoming frame
Outgoing frame
delay
time [s]
traffic

---
Cut-through Switching
- Receive whole frame before forwarding
- Start forwarding as soon as MAC header is received
Incoming frame
Outgoing frame
delay
time [s]
Incoming frame
Outgoing frame
delay
time [s]

---
End-to-end Delay Validation
- Propagation time = 50ns
- Transmission time = 1254B * 8 / 1Gbps = 10.032us
- Cut-through delay = 22B * 8 / 1Gbps = 176ns
- Store-and-forward end-to-end delay =
  3 * (Transmission time + Propagation time) = 30.246us
- Cut-through switcing end-to-end delay =
  1 * Transmission time + 3 * Propagation time + 2 * Cut-through delay = 10.534us

---
Covered Topics
Cut-through switching
Frame preemption
Per-stream filtering and policing
Scheduling and traffic shaping
Automatic gate schedule configuration
Time synchronization
Frame replication and elimination for reliability

---
Long Frame Problem
- Long frame delays high priority frame
- Express frame waits in the queue
Normal priority frame
Express frame
Time [s]
Express frame becomes available
normal and high-priority traffic

---
Frame Preemption
- Long frame delays high priority frame
- Reduce latency by interrupting transmission
Normal priority frame
Express frame
Time [s]
Express frame becomes available
Fragment 1
Express frame
Fragment 2
Interrupt transmission
Time [s]
Express frame becomes available

---
Covered Topics
Cut-through switching
Frame preemption
Per-stream filtering and policing
Scheduling and traffic shaping
Automatic gate schedule configuration
Time synchronization
Frame replication and elimination for reliability

---
Incoming Excess Traffic
- Excess traffic contends with other streams
- Introduces unpredicatable latency and jitter
- Violates end-to-end delay guarantees
normal traffic
excess traffic
oversubscribed link

---
Per-Stream Filtering
- Classify packets
- Shape streams with token-bucket coloring
- Enforce policing actions
- Minimizes cross-stream interference

---
Covered Topics
Cut-through switching
Frame preemption
Per-stream filtering and policing
Scheduling and traffic shaping
Automatic gate schedule configuration
Time synchronization
Frame replication and elimination for reliability

---
Outgoing Traffic Contention
- Priority queueing is insufficient
- Time-critical frame must wait ongoing transmission
- Introduces unpredicatable latency and jitter
- Violates end-to-end delay guarantees
high-priority traffic
best-effort traffic

---
Time-Aware Shaping
- Suitable for scheduled application traffic
- Periodic gate schedules
- Sets up a “green wave”
- Provides deterministic latency and jitter

---
Covered Topics
Cut-through switching
Frame preemption
Per-stream filtering and policing
Scheduling and traffic shaping
Automatic gate schedule configuration
Time synchronization
Frame replication and elimination for reliability

---
Manual Gate Schedule Configuration
- Designing an efficient schedule is hard
  - Cyclic dependencies, resource constraints
  - High complexity, scalability issues, error prone
- Poor schedule leads to large delay and jitter
- Difficult to ensure end-to-end guarantees
both traffic
both traffic
best-effort traffic
high-priority traffic

---
Automatic Gate Schedule Configuration
- Takes into account
  - Network topology
  - Traffic flows
  - Timing constraints
  - Optimization criteria
- Calculates gate schedule using a SAT solver
- Ensures bounded end-to-end delay and jitter

---
Covered Topics
Cut-through switching
Frame preemption
Per-stream filtering and policing
Scheduling and traffic shaping
Automatic gate schedule configuration
Time synchronization
Frame replication and elimination for reliability

---
Imperfect Clocks
- Application traffic and gate schedules follow clocks
- Clocks diverge
- Disrupts time-aware shaping
🕛
Clock 1
clock time [s]
Perfect clock
Clock 2
🕛
time [s]
🕛
🕛

---
Time Synchronization (gPTP)
- Shared time base
- Master-slave hierarchy
- Time dissemination
- Link delay measurement
- Continuous clock correction
- Stability and convergence
🕛
🕛
🕛
🕛
sync
sync
sync

---
Covered Topics
Cut-through switching
Frame preemption
Per-stream filtering and policing
Scheduling and traffic shaping
Automatic gate schedule configuration
Time synchronization
Frame replication and elimination for reliability

---
Node Failure
- Node failure causes packet loss
- Critical traffic is not allowed to lose packets
- Networks are unprotected against failures by default
traffic
traffic
traffic
traffic

---
Frame Replication and Elimination
- Replicate frames over multiple paths
- Identify stream split and merge points, eliminate duplicates
- Auto-configuration for specified node failure protection
traffic
traffic
traffic
traffic
traffic
traffic
traffic
traffic
traffic

---
Costs and Benefits
- Benefits
  - No packet loss or recovery delay on failure
- Costs
  - Negligible end-to-end delay increase
  - Increased configuration complexity
  - May need additional switches and links
  - May increase end-to-end delay for other streams

---
Try it Yourself
$ pip install --upgrade pip
$ pip install opp_env
$ opp_env init -w inet-workspace
$ cd inet-workspace
$ opp_env install inet-git@topic/wfcs2025 omnetpp-6.2.0pre1
$ opp_env shell
$ omnetpp
inet.omnetpp.org

---
Questions and Answers
Thank you for your attention!
WFCS – June 10-13, 2025
Levente Mészáros